## Slide 1
⛑
Shield-Sense
Smart Safety Construction Helmet
IoT Project Progress Report | ESP32 + Firebase
Real-time Environmental Monitoring for Construction & Mining Safety

## Slide 2
Project Overview
THE PROBLEM
Traditional helmets only provide physical protection
No real-time monitoring of surrounding environment
Workers unaware of gas leaks, heat stress, or falls
Delayed emergency response costs lives
OUR SOLUTION
ESP32 microcontroller with 3 IoT sensors
Live gas, temperature, humidity & fall detection
Firebase RTDB + Firestore for real-time data & logs
Web dashboard for operators to monitor workers
Shield-Sense | Smart Safety Helmet

## Slide 3
Hardware Components
E
ESP32
Main Microcontroller
WiFi-enabled brain of the system. Reads all sensors every 3s and pushes data to Firebase.
M
MQ-2 Gas Sensor
Gas Detection
Detects LPG, smoke & CO. Requires 5V from MT3608 boost converter for heater element accuracy.
M
MPU6050
Fall Detection
3-axis accelerometer measuring G-force. Communicates via I2C on GPIO21/22.
D
DHT11
Temp & Humidity
Monitors ambient temperature (alert >45C) and humidity (alert >85%) on GPIO4.
Estimated Total Cost: INR 1,610 - 2,450 (includes power supply, boost converter & helmet base)
Shield-Sense | Smart Safety Helmet

## Slide 4
Wiring & Connections
MQ-2 Gas Sensor
VCC
VIN (5V)
GND
GND
AO
GPIO34
DHT11 Sensor
VCC
3.3V
GND
GND
DATA
GPIO4
MPU6050
VCC
3.3V
GND
GND
SDA
GPIO21
SCL
GPIO22
Power Supply Chain
18650 Battery
->
TP4056 Charger
->
MT3608 (5V Boost)
->
ESP32 VIN
Important: All sensor GNDs must share common ground with ESP32 GND
Shield-Sense | Smart Safety Helmet

## Slide 5
Libraries Used
WiFi.h
Built-in ESP32
Handles WiFi connection of the ESP32 to local network for internet access
Firebase_ESP_Client.h
by Mobizt
Main Firebase library — connects to RTDB and Firestore, handles auth tokens
TokenHelper.h / RTDBHelper.h
Firebase addons
Helper utilities bundled with Firebase library for token management and RTDB operations
DHT.h
by Adafruit
Reads temperature and humidity values from the DHT11 sensor
MPU6050.h
by Electronic Cats
Reads raw 3-axis acceleration values from MPU6050 over I2C for fall detection
Wire.h
Built-in Arduino
I2C communication protocol library — required for MPU6050 on SDA/SCL pins
Shield-Sense | Smart Safety Helmet

## Slide 6
Firebase Architecture
ESP32
Reads Sensors
Firebase RTDB
Live Values
Web Dashboard
Live Monitoring
Alert
Triggered
Firestore
Alert Logs
Dashboard
Alert History
-> every 3s
-> live sync
-> log alert
-> history
Firebase Project: shield-sense | RTDB: asia-southeast1 | Auth: Email/Password | Firestore: (default)
Shield-Sense | Smart Safety Helmet

## Slide 7
Build Steps — Progress Till Now…
1
Hardware Assembly
DONE
Mount MQ-2, DHT11, MPU6050 on helmet. Wire all sensors to ESP32 per GPIO pin map.
2
Individual Sensor Testing
DONE
Test each sensor with simple Arduino sketches, verify correct readings in Serial Monitor.
3
Combined ESP32 Code
DONE
Full sketch reading all 3 sensors every 3s, with fall detection via G-force thresholds.
4
Firebase Setup
DONE
Created Firebase project 'shield-sense', enabled RTDB (asia-southeast1), Firestore and Auth.
5
ESP32 to Firebase Push
IN PROGRESS
Integrated Firebase_ESP_Client library. RTDB live push working. Firestore logs in progress.
6
Web Dashboard
IN PROGRESS
Build Login, Live Monitoring, and Alert History pages using Firebase JS SDK.
Shield-Sense | Smart Safety Helmet

## Slide 8
Alert Conditions & Thresholds
MQ-2 Gas Sensor
Gas > 400
Gas > 600
Log 'gas_leak_warning' or 'gas_leak_danger' to Firestore alerts collection
DHT11 Temperature & Humidity
Temp > 45C
Humidity > 85%
Log 'high_temperature' or 'high_humidity' alert with value to Firestore
MPU6050 Accelerometer
G-force > 2.5G
G-force < 0.3G
Log 'fall_detected' — spike indicates impact, freefall indicates fall
Shield-Sense | Smart Safety Helmet

## Slide 9
Applications & Real-World Impact
Construction Sites
Monitor workers in real-time for gas leaks, heat stress, and fall accidents on active build sites
Mining Operations
Detect toxic gases instantly and alert operators before dangerous underground buildup occurs
Industrial Plants
Continuous safety monitoring in environments with chemical exposure or high fire hazard risk
Emergency Response
Firefighters and rescue teams tracked for falls, freefall incidents, and hazardous air quality
Shield-Sense | Smart Safety Helmet

## Slide 10
Current Limitations
WiFi Dependency
Requires stable WiFi — no offline mode. If signal drops, data stops being logged to Firebase.
Battery Life
Single 18650 cell provides limited runtime. Continuous WiFi and sensors drain battery faster.
DHT11 Accuracy
DHT11 has +/-2C and +/-5% humidity tolerance. Not suitable for ultra-precise measurements.
MQ-2 Warmup Time
Sensor needs 2-3 minutes warmup before reliable readings — early values may be inaccurate.
Fall Detection Tuning
G-force threshold may trigger false positives for sudden head movements like nodding or jumping.
Firebase Security
Currently running in test mode with open rules — must be locked down before real deployment.
Shield-Sense | Smart Safety Helmet

## Slide 11
Next Steps
01
Fix Firestore Logging
Resolve Firebase Auth for Firestore using email/password — testing createDocument with user credentials
02
Build Web Dashboard
HTML/CSS/JS frontend with Firebase SDK — Login, Live Monitoring, and Alert History pages
03
Tune Fall Detection
Calibrate G-force thresholds to reduce false positives from normal head movements
04
Battery Optimization
Implement deep sleep between readings to significantly extend battery life
05
Secure Firebase Rules
Lock down RTDB and Firestore rules so only authenticated users can read and write data
Shield-Sense | Smart Safety Helmet

## Slide 12
SS
Shield-Sense
Smart Safety Construction Helmet
ESP32 . MQ-2 . DHT11 . MPU6050 . Firebase . IoT
Thank You!