## Slide 1
संप्रेषित-३.o २०२५ कल्पना की उड़ान, कला का संचार
Branch: ECS & EXTC Group No.
Shield-Sense
■ HARDWARE USED ESP32 (Main Controller) MQ-2 Gas Sensor DHT11 Temp & Humidity Sensor MPU6050 (Fall Detection) 18650 Battery + XL6009 Boost Converter Active Buzzer + Slide Switch
Prototype Photo
Circuit Diagram
● ESP32-based smart helmet Real-time monitoring of: ~ Gas levels (MQ-2) ~ Temperature & humidity (DHT11) ~ Fall detection (MPU6050) ~ Firebase cloud integration ~ Live web dashboard for supervisors ~ Buzzer alert on threshold breach
● ALERT CONDITIONS Gas Level > 400 → Warning Gas Level > 600 → Danger Temperature > 45°C Humidity > 85% Fall Detection via G-force Buzzer beeps until danger clears
● TECH STACK Firmware: Arduino C++ (ESP32) Cloud: Firebase RTDB + Firestore Auth: Firebase Email/Password Dashboard: HTML + CSS + JS Hosting: GitHub Pages atharva-patil9.github.io/shield-sense-dashboard
■ APPLICATIONS Construction Sites Mining Industry Industrial Plants Fire & Rescue Operations Emergency Response Teams
■ WIRING SUMMARY MQ-2 VCC → XL6009 OUT+ (5V) DHT11 / MPU6050 → ESP32 3.3V MQ-2 AO → GPIO34 DHT11 DATA → GPIO4 MPU6050 SDA/SCL → GPIO21/22 Switch → Battery(+) & Booster IN+ Buzzer(+) → GPIO2
■ LIMITATIONS Requires internet connection (WiFi) Battery dependent (18650 Li-ion) Needs sensor calibration MQ-2 requires 5V boost converter DHT11 has ±2°C accuracy tolerance
□ ADVANTAGES Improves worker safety Real-time buzzer & dashboard alerts GitHub Pages — accessible anywhere
● FUTURE IMPROVEMENTS Add GPS tracking Multi-helmet support Add offline functionality